## Slide 1
PROBLEM STATEMENT PQC-02 · AUTOMOTIVE HIL
Post-Quantum OTA Security for Vehicles.
Dual-role cryptographic firmware authentication (NIST FIPS 204 ML-DSA-44 + Ed25519 + Falcon-512) and hardware NVS anti-rollback running in 71.4 ms on bare-metal ESP32 silicon.
17.7 ms
ML-DSA-44 Verify
4,248,000 cycles @ 240 MHz
666 B
Falcon-512 Director
Fits in 11 CAN-FD 64B frames
36.5 KB
Peak Task Stack
6.85% of 520 KB SRAM budget
ML-DSA-44
2,420 B · 17.7 ms
Ed25519
64 B · 34.0 ms
OEM Hybrid 2FA Gate
2/2 Signatures Valid
NVS Monotonic Gate
SV 2 > Installed SV 1
ESP32-LX6 · SHA3-256
Atomic Swap -> Slot B (ota_1)

## Slide 2
01 // THE PROBLEM (PQC-02)
Why Automotive OTA Needs Hybrid Post-Quantum Auth
Vehicles operate for 15–20 years on the road, but embedded ECUs cannot run naive post-quantum schemes.
AutoQrpt · PQC-02
01 // SHOR'S ALGORITHM & HNDL
20-Year Road Exposure
Adversaries capturing wireless OTA traffic today can forge classical RSA and ECDSA/Ed25519 signatures once Cryptanalytically Relevant Quantum Computers (CRQCs) arrive during a vehicle's operational life.
Impact: Arbitrary remote code execution on braking, steering & ADAS ECUs.
02 // CRYPTOGRAPHIC AGILITY RISK
Pure PQC Is Not Enough Alone
Automotive OEMs cannot drop classical cryptography overnight—if an algebraic lattice shortcut is discovered in a standalone PQC primitive, a single-algorithm system fails open.
Requirement: Zero-fallback PQ/T Hybrid 2FA where both classical & PQC must pass.
03 // EMBEDDED SILICON LIMITS
520 KB SRAM & 64B CAN-FD Frames
Large post-quantum keys and signatures overflow microcontroller task stacks and flood 64-byte CAN-FD arbitration buses, starving safety-critical real-time vehicle frames.
Target: < 40 KB stack peak and compact CAN-FD frame budget on 240 MHz silicon.

## Slide 3
02 // SYSTEM ARCHITECTURE
Uptane Two-Role Separation + PQ/T Hybrid 2FA
Separating air-gapped OEM code signing from online Fleet Director vehicle targeting.
AutoQrpt · PQC-02
STAGE 01
QpiAI Quantum QRNG
8-Qubit Hadamard circuit (H^8 |0>^8, 1,024 shots) mixed with os.urandom(32) via SHA3-256. Shannon Entropy: 7.815 bits Min-Entropy: 6.54 bits
256-bit Root Seed
STAGE 02 · OFFLINE HSM
Air-Gapped Image Role
Signs 'AQ-IMAGE-V1' || manifest using: • NIST FIPS 204 ML-DSA-44 (2,420 B) • RFC 8032 Ed25519 (64 B) Even if cloud servers are breached, attackers cannot sign code.
2,484 B Dual Signature
STAGE 03 · ONLINE HSM
Fleet Director Role
Signs 'AQ-DIRECTOR-V1' || 'VEH-1' || manifest using NIST Round 3 Falcon-512. Compresses vehicle targeting into 666 B (11 CAN-FD frames).
666 B · 11 CAN-FD Frames
STAGE 04 · ESP32-LX6
Silicon Gate & Swap
Verifies NVS counter + all 3 signatures in RAM before erasing Slot B. Streams 4 KB chunks with SHA3-256 and swaps ota_0 <-> ota_1.
71.4 ms Total Verify

## Slide 4
03 // DETERMINISTIC WIRE PROTOCOL
Inside the 3,262-Byte .aqpk Frame Header
Every byte matches firmware/main/main.c — fitting 3 signatures + manifest into 51 CAN-FD 64B frames.
AutoQrpt · PQC-02
0x0000..0x0003
AQPK Magic
4 B
0x0004..0x006F
Manifest (AQM1)
108 B
0x0070..0x0309
Falcon-512 Director Sig
666 B (11 Frames)
0x030A..0x0349
Ed25519 Sig
64 B (1 Frame)
0x034A..0x0CBE
NIST FIPS 204 ML-DSA-44 Sig
2,420 B (38 Frames)
108-Byte Packed Manifest (AQM1)
• target_id[16]: 'ESP32-ECU-GW' (prevents cross-ECU flashing) • version[16] & uint32 security_version (checked against NVS 0x9000) • 3 x 8-Byte Pinned Public Key IDs (SHA3-256(pk)[:8]) • 32-Byte FIPS 202 SHA3-256 Digest of the firmware binary
Lockstep 4,096-Byte Chunk Handshake
1. Host sends 3,262 B header; ECU verifies all 3 signatures in RAM. 2. Only after 3/3 pass does ECU erase inactive slot & emit 'AQ:SEND'. 3. Host streams 4,096 B chunks; each is acked with 'AQ:ACK <bytes>'. 4. Final streaming SHA3-256 digest is matched before A/B boot swap.

## Slide 5
04 // VERIFICATION PIPELINE TREE
Five Hardware Gates Before Partition Activation
Zero-fallback invariant: a single failed gate halts execution and retains the active golden partition.
AutoQrpt · PQC-02
GATE 01 · HEADER
AQPK Magic Target & Key IDs
GATE 02 · NVS
Anti-Rollback SV > Installed
GATE 03 · DIRECTOR
Falcon-512 Verify 4.9 ms · 5.1 KB Stack
GATE 04 · OEM 2FA
ML-DSA-44 + Ed25519 17.7 ms + 34.0 ms
GATE 05 · COMMIT
SHA3-256 Stream 14.8 ms · 0 B Heap
ALL PASS
Activate Slot B (ota_1)
ANY FAIL
Retain Slot A (Zero Downtime)

## Slide 6
05 // PHYSICAL HARDWARE BENCHMARKS
Measured on ESP32-LX6 Silicon (240 MHz, 520 KB SRAM)
Captured over USB-UART (COM7 @ 921600 baud) using esp_cpu_get_cycle_count() and uxTaskGetStackHighWaterMark().
AutoQrpt · PQC-02
Cryptographic Verification Latency (10-Run Hardware Median)
Falcon-512 Director Verify
4.9 ms (4,914 us · 5,100 B stack)
SHA3-256 Streaming Digest
14.8 ms (Streamed · 0 B heap)
ML-DSA-44 Image Verify
17.7 ms (17,657 us · 36,496 B stack)
Ed25519 Classical Verify
34.0 ms (33,978 us · 2,304 B stack)
17.7 ms
ML-DSA-44 is 2x Faster than Ed25519
4,248,000 clock cycles on Xtensa LX6
36,496 B
6.85% of 520 KB SRAM Budget
483.5 KB SRAM remains free for ADAS/RTOS
51 Frames
Complete 3,262 B Header on CAN-FD
38 ML-DSA + 11 Falcon + 1 Ed25519 + 1 AQM1

## Slide 7
06 // ADVERSARIAL ISOLATION
17/17 Hardware-in-the-Loop Attack Vectors Blocked
Every rejected package leaves the active running slot (ota_0) 100% unchanged.
AutoQrpt · PQC-02
01_genuine_oem_release_v2.0.aqpk
Valid OEM Dual-Signed Update
ALL_CHECKS_PASSED
ACCEPT -> ota_1
02_faulty_release_v3.0_boot_crash.aqpk
Valid Signatures, Crashes on First Boot
BOOTLOADER_ROLLBACK_FROM_v3.0.0
AUTO ROLLBACK
03_tampered_firmware_bitflip.aqpk
1 Bit Flipped in 274 KB Payload
IMAGE_DIGEST_MISMATCH
REJECT (Gate 05)
04_forged_mldsa44_quantum_attack.aqpk
Signed with Rogue Attacker ML-DSA-44 Key
IMAGE_MLDSA44_SIGNATURE_INVALID
REJECT (Gate 04)
05_downgrade_replay_v1.0.0.aqpk
Validly Signed Older v1.0.0 Replayed
ROLLBACK_ATTACK_DETECTED
REJECT (Gate 02)
06_wrong_vehicle_VEH2_target.aqpk
Valid Director Auth, Targeted for VEH-2
DIRECTOR_FALCON512_SIGNATURE_INVALID
REJECT (Gate 03)

## Slide 8
07 // LIVE DEMONSTRATION
Unified OTA Firmware Deployment Portal
Drag and drop real .aqpk bundles in the live console — or flip 1 byte in RAM to trigger silicon rejection.
AutoQrpt · PQC-02
Live Hardware-in-the-Loop Verification Proof
1. Upload 01_genuine_oem_release_v2.0.aqpk -> All 5 tree gates pass in 71.4 ms -> ECU activates Slot ota_1 (SV 2). 2. Upload the exact same v2.0.0 file a second time -> Gate 02 (NVS Monotonic Counter) blocks it immediately as a replay (SV 2 <= 2). 3. Click 'Flip 1 Byte in RAM' on any valid bundle -> Gates 01–04 pass, Gate 05 (Streaming SHA3-256) catches the 1-bit corruption and aborts partition swap.
AUTOQRPT · QUANTUM-RESILIENT AUTOMOTIVE OTA